# System Setup
## Essentials Model Reference:
The Essentials model reference is a dictionary that contains the shell instructions on how to build assets. The information includes
- Name: Symbol {identical to the key}
- Type: String
- Measurements: Dict{Symbol, String}
- Components: Dict{Symbol, String}
- Specifications: Dict{Symbol, Any}
- LowerBounds: Dict{Symbol, Float}
- UpperBounds: Dict{Symbol, Float}
- MeasUnits: Dict{Symbol, String}
Templates are basically an easy dictionary input we get from the essentials model.
## Julia Assets:
These are actual “mutable struct” definitions of every asset type. They must directly map to the “Type” parameter from the Essentials template. Their “type” contains all the type information from the Essentials model and will trigger Julia’s efficient multiple dispatch. Each template should live in its own file, containing
1. The state definition
  1. The name of the current object (Symbol)
  2. The states of the current object
  3. State of each component
2. The object definition
  1. The list of core states of the current object (for indexing)
  2. Measurements (State{String})
  3. LowerBound (State{Float})
  4. UpperBound (State{Float})
  5. Conversions (Sate{Float})
  6. Specifications
3. The associated functions
  1. Mass balance functions
  2. Energy balance functions
  3. Prediction functions
  4. State-filling functions (which are similar to prediction)
  5. State dumping functions (which are universal and a simple application of the indexer)
## Asset States:
Asset states are trimmed down versions of a Julia Asset. States contain:
- Name :: Symbol (for dispatch reasons, to distinguish from string measurements)
- Measurements (Key States Only) :: T<:Union{String, Real}
- Components :: ComponentState{T}
- Specifications :: AssetSpecifications
Types formats in the state definition can take various forms:
- String (refers to an asset or measurement name)
  - Used for building the BOM, and mapping indexers
- Real (refers to an asset value, can be a float or dual number)
  - Used to evaluate mass balance error and to define value boundaries and prediction values on the state vector
- Index (refers to an index of the state vector, 0 if it doesn’t use the state vector)
  - Used to map between state vectors and assets
Asset states should be mutable objects for the following reasons
1. One can easily reuse code for an asset’s parent for state indexing. If objects are immutable, you need to copy the parent object’s result.
2. There is a lot of reference data that needs to not change, Specifications is a big one. Explicitly passing all the specifications every time we touch a state is very cumbersome.
3. Predictions often reassign only a few states.
4. It’s the cleanest way to avoid input output confusion when performing a prediction
  1. You COPY the input streams from the BOM
  2. You REFERENCE the output streams (so you can update the BOM)
  3. This ensures that outputs from one model don’t affect the inputs from the other, and that the simulation updates the correct elements of the BOM.
Components (for ProcessUnit_Type), for the most part, consist of streams. There may be other components such as stages (as seen in a compressor or distillation column) that are not connected by streams. Any asset connected to its parent by a stream (such as a reboiler on a distillation column) is considered a completely separate asset.
## Dimension Reduction: Key states, fill others only as needed
This was already discussed previous, but the point of constructing a state from a minimal set is primarily to enforce nonlinear constraints and facilitate the problem through dimension reductions. As an example, for streams it is useful to have a core set of base states that the entire object can be calculated from.
- Temperature
- Pressure
- Mass flow of each component
This core set of states can be mapped to the vector, and this is what is kept inside each asset. Other values (such as Cp and Density) are only calculated when they need to be. Even if calculations are repeated, it’s more efficient then calculating everything and storing because
1. Repetitions would be much fewer than calculating the whole state
2. Repetitions would be done in parallel anyway (both predictions and measurements)
3. Required data is heavily contingent on the connecting processes
4. Data required for predictions is often very different than data required for measurements
## Hierarchy to Vector Mapping
Each object will have its own indexer type. The indexer is used to map between the state vector and the objects. This indexing scheme will be called every iteration and it is thus performance-critical. However, iterating over field names at runtime is not performant. In such a case, generated functions may be desirable.
- https://discourse.julialang.org/t/how-to-write-a-fast-loop-through-structure-fields/22535
- https://docs.julialang.org/en/v1/manual/metaprogramming/
For a generic asset mapping from vector to structure, you would need to write a generated function that would look similar to this:
@generated function update_state_struct!(s :: AbstractAsset, v::Vector, ind::T) where T
    ex = Expr(:block)
    for fn in keystates(T)
        push!(ex.args, :( s.$fn = v[ind.$fn])
    end
    for fn in components(T)
        push!(ex.args, :(update_state_struct!( s.$fn, v, ind.$fn )))
    end
    return ex
end
We would also need to call a special version for streams as their components would depend on the value of the “type” field on the stream.
function update_state_struct!(s::ProcessStream, v::Vector, Ind::ProcessStream)
    update_state_struct!(s, v, ind, ind.Type)
end
function update_state_struct!(s::ProcessStream, v::Vector, Ind::ProcessStream, ::Type{T}) where T <: ProcessStream_Generic
    ex = Expr(:block)
    for fn in keystates(ProcessStream)
        push!(ex.args, :( s.$fn = v[ind.$fn])
    end
    for fn in stream_components(T)
        push!(ex.args, :( s.mass_flows.$fn = v[ind.massflows.$fn] )
    end
    for fn in setdiff( fideldnames(StreamComponents), stream_components(T) )
        push!(ex.args, :( s.mass_flows.$fn = 0)
    end
    return ex
end

## Bill of Materials (BOM):
The Bill of Materials contains all the assets of a system. It can be represented as a NamedTuple or dictionary of Julia Assets. There are 3 main types of BOM
1. A dictionary of Asset_Type{String} to map to Essentials/Data Broker. This is typically a dictionary as flexibility is more important than speed here (only need to construct it and refer to it once, but we need to do it iteratively).
2. A named tuple of Asset_Type{Int32} that contains the equivalent index of the state vector.
3. A named tuple of Asset_Type{Real} that contains the state vector data (even possibly dual numbers when optimizing).
In order to facilitate constructing these NamedTuples, we will need a couple of functions:
1. dict2namedtuple (easy construction of named tuples from pairs can be seen below)
  1. (; zip(keys, values)...)
  2. (; generator_expression()...)
2. convert_base_type(T, OldAsset)
  1. For actual base type
  2. For assets
  3. For Iterable Collections
When the state vector changes, we go through 1 neccessary step and one optional step
1. Assign the state vector values to key states. This is also inexpensive and can be hierarchically done, redundancy isn’t a huge issue, but multi-threading is
2. Make state predictions or instrument validations
  1. State predictions may require some intermediate state calculations (like heat capacity)
  2. Instrument validations may require other intermediate state calculations (like volumetric flow and density)
  3. Not all streams need all things, so time would probably be saved by using the measurement and prediction functions to calculate any intermediate states they need
If we are doing this on a single core, we could do a once-through hierarchical calculation where we update all children before updating a parent. If we are using multi-threading, we’re better off doing multiple single-level passes in order to avoid race conditions.
1. Start a for loop according to the number of assets in the BOM
2. Filter out the asset names (names are type-stable and are in bounds) that are updated
3. Update all remaining asses whose (BOM) children are updated
4. Stop if
  1. If the remaining asset set is still the same (no progress)
  2. If the name set is now empty
5. Perform a parallel hierarchical update on all remaining asset names
At every pass, we filter out the asset names that are updated and only update assets whose children have all been updated. The passes are finished when filtering yields empty results.
## Streams Types with Type Labels
In order to prevent a proliferation of types, streams must have an inner component (called Components) that have a list of all possible stream components in the BOM. However, we do not need to use all components. The component object of each stream can have a label containing an abstract Type object (such as “Mined_Solids_Stream”) that would indicate
- What components are relevant to the state vector (and what are forced as zero)
- How properties like Density and Cp are defined
This could then be used to dispatch calculations based on the abstract type inside the label. This allows us to have one stream type (stabilizing the type information of all objects that use streams) while at the same time giving flexibility on stream calculations.
## Assemblies
Assemblies are special assets that contain other assets in the bill of materials. Assets are meant to be separated from other assets though streams. An assembly is meant to be composed from a group of assets. In fact since assets are mutable, assemblies are merely a way to refer to existing assets (think of a distillation unit referring to a tower, a condenser and a reboiler as well as all the connecting streams).
Assemblies are meant to serve as logical groupings in order to calculate key performance indicators. As such, assemblies should be generic and have swappable components. KPI calculations are not performance-heavy, so it may be possible to make an assembly object with abstract fields. Otherwise, assemblies may have to be parametric types with the first parameter being the numeric type (such as Int or Float), with the rest of the parameters defining the internal equipment types.
## Internal Components
Most components of an asset will show up in the BOM; in particular, streams as they will be assigned to other pieces of equipment and have measurements attached to them. However, in some cases it makes more sense for the components not to show up in the BOM as they are an intrinsic component. For example, a distillation tower with a side feed will consist of a feed stage, a stripping section (below the feed) and a rectifying section (above the feed). These are intrinsic “areas” of the same column but are modelled as distinct components. Intrinsic components should be distinguished by having the name “None”.
Additionally, some separable components like a motor shaft may not need to show up in the BOM because they have no real measurements. For a shaft, any equipment attached can simply assign their shaft to be the same as the motor, the shaft itself can have a field name “driver” which points to the parent motor or turbine.
## Canonical Tower Units (Distillation, Strippers, Absorbers)
The canonical distillation column could be a “more complicated two phase separator”. The mass balance variables are simply the fraction of inlet escaping through gas. Stripper and Absorber mass balance veriables are also summarized by fraction of inlet escaping through gas. All cases can be solved by defining an nC element vector of “K-values”
K[i] = gas_mole_fraction[i]/liquid_mole_fraction[i]
K[i] = nG[i]/nL[i] * RL => RL = sum(nL)/sum(nG)
However, this results in a nonlinear mapping to
ɣ[i] = gas_outlet_mass[i] / total_inlet_mass[i]
It is much easier to map from ɣ[i] to K[i] rather than the other way around. To go the other way around, you first need to calculate the mole fractions of the outputs which is iterative:
1. Assume RL = 1
2. nL[i] = RL*n[i] / (RL + K[i] )
3. nG = nT – nL (nT is total inlet, nG is gas outlet, nL is liquid outlet)
4. RL = sum(nL)/sum(nG)
5. Reiterate with new RL
For simple mass balance models however, it is simpler use ɣ[i] as the random-walk variable and enhance the models by predicting it.
## Custom Tower Units (Distillation, Strippers, Absorbers)
Given a number of input/size draw streams N, a tower can be divided into N+1 sections. If there is a side feed to a distillation column, we get two sections. The upper half is an absorber and the lower half is a stripper. Thus, side draws and side feeds cause a tower to become an assembly of more towers. Moreover, the location depends on the kind of feed or draw.
- Liquid feeds and Gas draws are at the top of the section
- Liquid draws Gas feeds are at the bottom of the section
Short of a few well-defined situations (such as a single liquid feed) a tower with arbitrary feeds and draws will require an internal bill of materials with a new type of asset:
- Feed tray: A junction of 3 input streams and 2 output streams
- Draw tray: A junction of 2 input streams and 3 output streams
A feed/draw tray is considered a “Superstream” where each of its internal streams are not part of the BOM, but link to the sections themselves. Phases of the feeds and draws will need to be determined by equations of state.
This approach simplifies the “Side Feed/Draw Tower Unit” to have two “Array” components,
- Array of N “Feed/Draw” trays (the type of which is denoted by a Boolean “is_feed” field)
- Array of N+1 “Simple Towers”
This allows the asset to be truly generic in the most efficient way possible.

## Inheritance (affects state-vector conversions and predictions)
An asset B is a child of A if B contains all the fields of A with some extras. Julia’s type system doesn’t allow subtyping of concrete types, so we need to make “parent” and “child” functions that return the applicable type. The main advantage of inheritance is being able to reuse code when transforming the model to a state vector and back again as well as making predictions.
Here is a code pattern to call the parent’s calculation routine:
#A function that calls the explicitly type-dispatched function
function predict_state!(Asset ::ShellAndTubeHX_Type)
predict_state!(Asset, typeof(Asset))
end
#A type-dispatched function that calls the type-dispatched parent routine
function predict_state!(Asset, ::T) where T == ShellAndTubeHX_Type
predict_state!(Asset, parenttype((Asset)))
...
end
#A type-dispatched function of the parent routine
function predict_state!(Asset, ::T) where T == HeatExchanger_Type
predict_state!(Asset, supertype(typeof(Asset)))
...
end

## Building Asset Subtypes
One method is to use Mixers.jl which essentially does what we want. This link also gives a macro on adding states:
https://discourse.julialang.org/t/inheritance-in-julia/5416/17
Such a technique results in two inheritance functions:
- One that inherits assets (which are paremetric types) and must exclude certain fields like “Specs”
- One that inherits specifications (which are not parametric types) and include all fields
The two macros are shown below and are called in the middle of a struct statement. This is a clean method that avoids external dependencies.

function get_type_expression(X::Union{Symbol,DataType})
    if X isa Symbol
        return X
    elseif X isa DataType
        Params = X.parameters
        if isempty(Params)
        return Symbol(X.name.wrapper)
        else
        return Expr(:curly, Symbol(X.name.wrapper), Params...)
        end
    end
end
macro inherit_asset_fields(AssetTypeExp::Expr)
    BaseAssetType = Core.eval(@__MODULE__, AssetTypeExp.args[1])
    TypeSymbols = AssetTypeExp.args[2:end]
    AssetType = BaseAssetType{TypeSymbols...}

    ex = Expr(:block)
    for fName in filter( x-> x!=:Specs, fieldnames(AssetType) )
        fType = fieldtype(AssetType, fName)
        fTypeParsed = get_type_expression(fType)
        push!(ex.args, :( $fName :: $fTypeParsed ) )
    end

    return esc(ex)
end

mutable struct MyOldType{T}
    Name :: Symbol
    A :: T
    B :: T
    V :: Vector{T}
    Specs :: String
end

mutable struct MyNewType{T}
    @inherit_asset_fields(MyOldType{T})
    C :: T
    NewSpecs::String
end
## Assemblies
Assemblies are useful for performing KPI calculations, but are not really integral to mass balance or data reconciliation. For mass balance purposes, if the child asset is connected through a stream, the stream is often sufficient (due to its Markov property). Thus we should only really need streams of the current asset. The only time way may need components is if there are components that are not part of the stream.
Because of this, assemblies should usually be decomposed into their assets and added to the BOM. KPI’s could later be performed by reconstructing assemblies from the BOM.
# Data Reconciliation Strategy
## Parallel Predictions
Each unit can take inputs from streams and the current state and predict outputs. These outputs then feed to other pieces of equipment. In order to enable parallelization, we will need to ensure that output states don’t overwrite input states. Thus the predict function will require three arguments:
function predict_state!(outputState, inputState, dispatchType)
In order to account for the fact that the output of one process feeds into another we can have a consistency error term for stream predictions: (x-f(x))/S*(x-f(x)). This moves the task of sequencing process units to the optimization algorithm.
In this way, the output predictions are stored in an independent mutable object (this also helps speed to prevent unneccessary preallocation). Additional convenience is found in that the optimization happens by modifying the input state, but the output state is used for the next iteration.
## State Estimation: Why Optimization is better
Using an optimization method gives us numerous advantages over the Kalman filtering method:
1. Constraints are better-reflected in the probability distribution (Kalman filtering is Gaussian and doesn’t handle constraints [truncated multivariate Gaussian] well)
2. We can maximize over the previous value instead of doing the propagation first (which helps better deduce accumulation steps)
3. Model is not approximated (UKF gives us at best an unconstrained 2nd order approximation)
## State Estimation: Objective Function
Let “x” be the state vector, “x0” be the previous state and “y” be a set of observations
- Deviation from prior
  - (x-x0)/(P+Q)*(x-x0)
- Steady-state stream consistency (additional “0” observations and absorb into R)
  - (x-f(x))/S*(x-f(x))
- Measurement error
  - (y-h(f(x)))/R*(y-h(f(x)))
- Total objective function
    - err = (h(f(x)) – y)’*inv(R)*(h(f(x)) – y) + (x-x0)’ inv(Q+P) * (x-x0)
    - J = Jacobian of h(f(x))
    - Gradient = J’*inv(R)*(h(f(x)) – y) + inv(Q+P) * (x-x0)
    - Hessian = inv(P) = J’*inv(R)*J + inv(Q+P)
- The only challenge is if f(x) contains some sort of inner optimization (such as iterative methods to solve a system of equations), we have to use the Envelope Theorem
  - https://discourse.julialang.org/t/a-hacky-guide-to-using-automatic-differentiation-in-nested-optimization-problems/39123
## State Estimation: Algorithms
At the time of writing, we are considering the Interior Point Newton algorithm or an active set Newton method. The interior point method exists in a package, but I would have to write an active set method myself. Active set methods clamp elements that violate the constraints, and if the next iteration requires constraint violations, the reduced set is solved.
Active set methods are easy to apply to box-constraints, and since similar problems are often solved with the EKF (which is a single-step Newton method), we might be able to apply a simple active set Newton method with little overhead.
Newton methods are preferred due to:
- Hessian calculations are only order “n” for State space models and you can get them for free when calculating gradients. Both gradients and Hessians can be calculated using the same Jacobean
- The only higher-order task is a matrix inversion. The problem should be separable enough to prevent matrix inversions from becoming too difficult.
- Function evaluations can be expensive, so we want a higher-order convergence

## State Estimation: Battery-Limit Streams
Process areas are fed and drawn from streams crossing a battery limit. These tend to be main lines connecting major areas. Such lines are often well-instrumented and connect to a buffer such as a tank allowing areas on each end of the line relatively independent operation. These are ideal points to break apart data reconciliation into smaller more manageable pieces (recall that we are using matrix inversions, and these are O(n3) so it makes sense to keep the dimension size reasonable).
While these streams can be used to break a system into manageable chunks, information in these streams can still have contributions from the neighbouring systems. This can be done using a standard Bayesian Gaussian update.
Update xt using x1 and x2 from systems 1 and 2
- Pt = inv( inv(Pt0) + inv(P1) + inv(P2) )
- xt = Pt*( inv(Pt0)*xt0 + inv(Pt1)*x1 + inv(Pt2)*x2 )
This new xt can also be Kalman filtered based on measurements.
## State Estimation: State Uncertainty Options
- Calculate the Hessian which happens to be inv(P)
  - Hessian = inv(P) = J’*inv(R)*J + inv(Q+P)
- EKF
  - Requires n function evaluations
  - Large number of second order matrix operations
  - Requires non-diagonal matrix inversion
- UKF
  - Requires 2n+1 function evaluations
  - Requires non-diagonal matrix inversion
## Dimension Reduction: Mass Flow (*Only at steady state)
Data reconciliation is subject to mass and energy balances closing but ONLY AT STEADY STATE. In our dynamic modelling, steady states are rarely achieved except for very fast processes. However, it is important to note that mass balance constraints are linear.
- Even chemical reactions are linear, as the additional state is an extent of reaction multiplied by a constant vector, resulting in a linear constraint to the mass balance states.
- Energy balances are only linear given a mass balances
  - m1*Cp*T1 + m2*Cp*T2 + Q = 0
  - T1 and m1 are two states that are combined
  - Energy balance models are less precise (as energy leakage can happen)
  - Energy balances could be introduced as error terms
- Nonlinear parts of the model are not exact and are often predictions; these lend themselves well to soft constraints (as is done in Kalman filtering)
If we let the mass balance error be calculated in the form
Err = (L x)
We can see that the summed squared mass balance error takes the form
Err2 = (x’L’)(Lx) = x L’L x
This means that the Hessian of the mass balance error (L’L) can be used to reduce the dimension of x.
λ, E = eigen(L’L) (λ=eigenvalues, E=eigenvectors)
In particular, the Eigenvalues of the Inverse Hessian inv(L’L) should result in a very sharp “scree plot” pattern; the Hessian should produce an inverse scree plot.
The non-zero Eigenvalues are latent variables that have reduced freedom of movement. Thus the eigenvalues are used to compute a linearly constrained state. Let λ be the set of reduced eigenvalues and E be the corresponding eigenvectors:
x = E * z (z = reduced set, where eigenvalues λ=0)
We could also add box constraints in linear form where
x_LB <= E z <= x_UB
While this does reduce the dimension of the problem, it means we no longer have box constraints (rotating it by eigen-transformation now tilts it). Because of this, we might need to use interior point methods. Fortunately, because the constraints are linear, the Jacobians should be E and the Hessians should be 0. Optim.jl has an interior point Newton method which should be sufficient for this purpose as the optimization is nearly quadratic (to the point where a Kalman filter is probably acceptable).
https://julianlsolvers.github.io/Optim.jl/stable/#examples/generated/ipnewton_basics/
https://www.youtube.com/watch?v=zm4mfr-QT1E

The recommended approach for this is therefore:
1. Have a mass balance error function for every process element
2. Calculate the Hessian of this mass balance model from the component mass flow states.
3. Create a reduced mass flow state for all stream mass flow components based on eigenvalues.
4. Use the eigenvectors to arrive at the full mass balance state from the reduced state.
## Reconciler Workflow:
1. Before startup
  1. Define the asset types and associated functions
    1. Fundamental States
    2. Calculated States
    3. Prediction function
    4. Infill function
    5. Mass balance error function
    6. Energy balance error function
2. At startup
  1. Build out the model
    1. String form of assets
    2. Indexers from string form
    3. Measurements from string form
    4. Fundamental State Boundaries from string form
  2. Build out the mass flow dimension reduction scheme
3. At each state transition
  1. Perform the transition mapping
    1. Build out the extended state from the mass-flow reduction
    2. Build out the fundamental states each item in the BOM
    3. Apply the prediction functions
    4. Rebuild the state vector from the predictions
    5. Output this state vector as a squared error prediction reference
  2. Calculate the initial guess from the squared error prediction reference
  3. Solve the nonlinear optimization problem; for every reduced state iteration
    1. Build out the extended state vector from the reduced state
    2. Calculate the prediction error
    3. Build out the fundamental states for each item in the BOM
    4. Build out the filled states for each item in the BOM
    5. Calculate the measurement error
    6. Calculate the energy balance error
  4. Obtain covariance matrices by linearizing the system around the optimal point, and use the square-root Kalman filter to obtain the posterior covariance.
  5. Output the extended state for KPI calculations and reconciled estimates
  6. Create assemblies for KPI evaluation (assemblies may as well be keyword-defined structures with abstract fields)
  7. Evaluate KPIs
## Inheritance:
If x1 is a subset of xn, we can call reconciler functions to trigger on x1, then x1’s parent and so on until we get to xn (which has a parent of “any”). For x1 to be a child of xn it must have all the same mass balance equations.
- The reconciler for x1 will call the reconciler for x1’s type-parent (x2)
- The reconciler for x2 will call the reconciler for x2’s type-parent (x3) and so on
## Add-on Analyses:
An add-on analysis (such as pump efficiency) could potentially be an additional Key Performance Indicator. KPIs are generally calculated values using the state as input; they do not feed additional information to the actual state. However, if the analysis might be able to explain some behaviour (such as corrosion), it would have to be added as a child node. Thus the error function for “centrifugal pump with corrosion” would invoke the following error functions
- “centrifugal pump corrosion”
- “centrifugal pump”
- “pump”
- “mass balance node”
This will have to be done based on type dispatch so that
funciton f(N<SpecificType>::GeneralType, ::Val{GeneralType})
Calls the same function as
funciton f(N<GeneralType>::GeneralType, ::Val{GeneralType})
Instead of
funciton f(N<SpecificType>::SpecificType, ::Val{SpecificType})
Otherwise the general type function will never get called
## Indexer Strategy:
Each asset model comes in three forms:
- Element Type = String, Maps ports to asset names / TSIDs
- Element Type = Integer, Maps ports to an index to a vector
- Element Type = Real, Maps ports to actual values
Indexing is a bit slow and cumbersome to code. We might actually be able to build an actual object with type T <: Real and pass dual numbers to it. This also means that process objects can be their own indexer! We should test this. If this is the case, then we simply run the indexer at the beginning of every iteration (using @inbounds for speed) and perform the mass balances over the objects (mass balances only read the state, the optimizer assigns them).
Optimization strategies require that the state be represented as a vector with no hierarchical information. This means that the state is actually a vector with a large number of values being passed around to the equipment error functions. The error functions use indexers to compute the error, and can thus be agnostic about the actual vector being passed around. It merely requires the indexer to point to the correct position in the vector.
Before instantiating any of the indexers, we need to define the custom indexer for the chemical component list for this reconciler (which will be a subtype of general chemical component lists). This will allow us to create the correct instance of streams and all the other assets as well.
We need a function to build an indexer from an asset type. We also need a function to build a populated model using an indexer and a vector.
The Essentials BOM for the reconciler obtained by getting the appropriate model info for all items in Essentials. There needs to be a routine that can generate an indexer for any equipment found in Essentials. Custom templates will need to feed a “type declaration” before use. Going through the Essentials BOM, one checks the Reconciler BOM to see if an indexer already exists. If not, the indexer is constructed and added to the Reconciler BOM. If a component of that asset doesn’t exist in the BOM, it must also be created. Thus, assets are created as needed, recursively.
Indexer fields can be one of three types:
- Union{String, Int64}
- Indexer
String indexers map to the data source/sink, while integer indexers map data to the reconciler vector.